## Slide 1: Challenges and Opportunities for Natural Gas in the Energy Transition
Ruud Egging
21 June 2019
2nd International Conference
The Economics of Natural Gas
Paris-Dauphine University
With support and material from Pedro Crespo del Granado (NTNU), Franziska Holz (DIW/NTNU), Péter Kotek (REKK), Borbála Tóth (REKK)

## Slide 2: Outline
NG - main drivers and general outlook
Challenges connected to NG
Opportunities/Possible roles for NG
Methodologies
Recent Work
Research challenges

## Slide 3: Main drivers and outlook

## Slide 4: EU climate strategy: building blocks
Need to decarbonize
  2050: 80% electricity RES, substantial electrification, role for nuclear
energy efficiency
  Industry, buildings
transport
  Electrification, alternative fuels, better transport management.
industry
  different fuels, carbon sequestration and use.
sustainable land use
  more biomass use, enhance forests and land as sinks
infrastructure essential
  facilitate energy systems integration and digitalization, use low-carbon fuels
carbon capture and storage
  necessary notably to decarbonise industry.

## Slide 5: Supply-side drivers - global
Plenty of supply, e.g.,
  Middle East conventional resources
  (US) shale gas
Increasingly more LNG exporters, and shorter distances
  Panama Channel + Northern Sea Route cut travel times

## Slide 6: Supply-side Europe
Europe
  Decreasing production
  Increasing imports
  Nordstream II in progress
  Norway only remaining European exporter
  PCI projects on hold

## Slide 7: Demand-side drivers
Upward
  Growing population
  Growing GDP
  Energy access
  Blue hydrogen
  Local air quality
  LNG in transport and shipping
  Need for large-scale back-up, flexibility and balancing
Downward
  Cost declines clean energy technologies
  Synthetic gas
Mixed
  GHG emissions
  Electrification
  CCS costs and acceptance
IEA, DIW, MIT

## Slide 8: «Not on track for Paris» Outlooks
Gas consumption + 40-50% to about 5000 bcm by 2040
Trade grows faster than consumption, LNG even more
Europe
  only region where production and consumption decrease.
  Imports likely to increase further
  Netherlands net importer? Much reduced swing from Groningen domestically and neighboring countries.
  Norway only major producer-exporter; flat production outlook
IEA, MIT

## Slide 9: WEO2017 Three Scenarios
+45%
+15%

## Slide 10: Challenges
Broader than the energy system – Climate, societial, …

## Slide 11
http://www.un.org/sustainabledevelopment/sustainable-development-goals/
Notes: WEO Intro chapter 3
end poverty, protect the earth and ensure prosperity - for all.
achieving universal energy access, limitng climate change and reducing air polluton, alongside enhancing energy security.

## Slide 12: The Paris Agreement
Keep global temperature increase below 2°C above pre-industrial level; aim limit to 1.5°C
https://unfccc.int/process/the-paris-agreement/the-paris-agreement

## Slide 13: Energy system specific challenges
Decarbonizing and decentralization in two-three decades
  need large volumes and capacities for backup, balancing and flexibility on various time scales
Today electricity storage other than hydro reservoirs too expensive
  Biomass.. (EMPIRE 2050). Availability? C-neutral w/o CCS?
For both Hydrogen and CCS
  Value chain still immature
  Public acceptance and perceived safety
  Chicken & Egg problem *
H2: low energy content hampers competitive long-distance transport
CCS: Norway only European country with activity
CCS on quickly ramping gas-power possible. But CCS capital intensive; many operational hours – bad match with peak shaving

## Slide 14: Other sectors - challenges
Industry - decarbonization:
  Feedstock
    NG for some processes preferred input. Hard to replace (by something cleaner).
  Process heat
    Heat pumps and electric furnaces need powered
  Inevitable emissions
    E.g., cement. Negative emissions elsewhere or CCS. CCS cheaper. (starting at 50-75 €/ton)
Transport – decarbonization
  Batteries are heavy / low-energy content
  Biofuels GHG impact unclear, biomass availability?
  Hydrogen… see previous
IEA, DIW

## Slide 15: NG roles
Does NG have a role in low-carbon decentralized energy systems?

## Slide 16: NG roles Europe – back of the envelope
Horizon Application | 2030 | 2050
Base-load power | Yes | Unlikely
Flexi power | Yes | Probably
IND - Feed stock | Yes | Probably
IND - Process heat | Yes | Probably
Building heating | Yes | Maybe
Transport | Segments | Possibly
Hydrogen feedstock | Yes | Probably

## Slide 17: Boundary conditions
What is needed to facilitate roles in the energy system?

## Slide 18: Boundary conditions for NG role
Application | Horizon: 2050
Base-load power | CCS Negative emissions elsewhere (NETs); eg, BECCS
Flexi power | No electricity storage break-throughs Remuneration of flexibility value CCS (?) / NETs elsewhere
Building heating | NETs elsewhere (Electrification more likely)
Transport | Negative emissions elsewhere
CH4+CCS=H2 | acceptance a market and infrastructure CCS
+ level-playing field for technologies considering all external effects including adequate market designs and timely and reliable policy environment

## Slide 19: NG and other energy carriers increasingly connected / integrated: analyses need wider scope than traditional models with single sector perspective can provide

## Slide 20: MethodologY - MODEL LINKING

## Slide 21: Three of the main model types
I.A.M.
C.G.E.
P.E.
Integrated Assessment Model
Computational General Equilibrium
Partial Equilibrium
Pix credit: Dreamstime.com

## Slide 22: Characteristics of some model types used for policy support and analysis
 | IAM | CGE | P.E.
Perspective | Holistic | Economy | (Energy) sector
Metrics and relations | Aggregate economic, technical & physical | Aggregate economic | Detailed economic & physical
Climate | + | - | -
Environment | + | - | -
Carbon cycle | + | - | -
Land use & forestry | + | - | -
Oceans & water | + | - | -
Economy & trade | + | + | -
Spatial detail | - | + | +
Technical detail | - | - | +
Temporal detail | - | - | +
For illustration only

## Slide 23: Let each model type do what it’s good at
Isolated
  Define consistent parameterizations for all models
  Run models
  Results inconsistent due to underlying assumptions
Integrated
  Develop one model combining all strengths of all models
  Necessarily sacrifice detail to maintain tractability
(Soft / Hard) Linked
  Decide relative strengths of each model and which (exogenous) inputs are based on (endogenous) outputs of others
  Define consistent parameterizations
  Iteratively run models and exchange data until results are consistent

## Slide 24: Linking models - why
No single model can covers all aspects in all desired detail.
Need consistent & coherent quantitative representations across models to analyze scenarios
Models have different
  Approaches
  Foci: strengths & weaknesses
  Scopes, scales / granularities & information structure
  Exogenous (parameters) vs endogenous variables / boundary conditions
  Physical vs monetary representation; units of measurement
  Features give complementary strengths but pose challenges for exchanging data
One model’s results are another’s boundary conditions

## Slide 25: Using relative strengths:
I.A.M.
C.G.E.
P.E.
Climate
Land use
Global trade
Emission ceilings / costs
Energy demand
Energy prices
Outputs
Prices

## Slide 26: Challenges when linking models:
Differences in
  Granularity (level of detail)
    Spatial
    Temporal
    Technical
  Scope
  Units of measurement
  Underlying assumptions
Version control
Convergence

## Slide 27: Linking models – how?
Middleware
  all models exchange with one central DB:
  Reduce number of links from M(M-1) to 2(M+2)
Upfront agreement on
  Technical, Spatial, Temporal resolutions
  Standardized data table formats
  Units of measurement
  Unique identifiers for data sets and entries
  Documentation of data
Automated scripts for hard-linking

## Slide 28: IIASA data exchange platform
Inputs and results
https://data.ene.iiasa.ac.at/set-nav/

## Slide 29: Decarbonization EU ENERGY SYSTEM – impact ON GAS

## Slide 30: H2020 SET-Nav April 2016 - March 2019
Navigating the Roadmap for Clean, Secure and Efficient Energy Innovation
SET-Nav EC H2020 grant 691843

## Slide 31
Case Study 7.4: Unlocking flexibility and synergy in electric power and natural gas supply systems
Pedro Crespo del Granado, Christian Skar, Hector Marañon Ledesma (NTNU); Blazhe Gjorgiev, Giovanni Sansavini, Andrea Antenucci (ETH Zurich); Luis Olmos, Quentin Ploussard, Sara Lumbreras, Andres Ramos (Univerisidad Pontificia Comillas)
The SET-Nav project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement no. 691843 (SET-Nav).

## Slide 32
Modelling framework

## Slide 33
Cases
All models calibrated to PRIMES decarboniz scenario (E3MLab & IIASA 2016)
Nuclear restricted [current cap levels; no replacement]
No CCS
Flexi-Grid - Transmission
  Transmission expansion allowed (Electricity)
  EMPIRE: intra-day demand response + curtailment
   Grid expansion & hydro main sources flexibility
Flexi-1 – electricity storage
  Transmission is restricted [current levels + 10Y ENTSO-E NW plan]
   More electricity storage and gas thermal plants.
Flexi-2 – gas infrastructure
  Transmission is restricted
  Electricity storage expensive
  Demand response (current levels)
   Gas thermal plants main flexibility provider.
E3MLab and IIASA (2016). Technical report on Member State results of the EUCO policy scenarios. EUCO 27 scenario. Energy Modelling, European Commission. https://ec.europa.eu/energy/en/data-analysis/energy-modelling

## Slide 34: EU power generation mix
gas
solar pv
wind onshore
nuclear
coal
lignite
hydro
w-offs
Gas primarily base-load in 2025; in 2050 balancing.
Utilization 64 (+/-1)% in 2025; 15% in 2050.

## Slide 35
Coauthors: Péter Kotek, Borbála Tóth (REKK), Franziska Holz (DIW), Pedro Crespo del Granado (NTNU)
PATHWAY ANALYSIS
THE ROLE OF NATURAL GAS IN AN ELECTRIFYING EUROPE

## Slide 36: Pathways

## Slide 37: Models
Demand sector models:
Buildings, Industry and Transport
Supply and Infrastructure models:
Power system, transmission grids, heat grids, gas sector and other incoming technologies (e.g. CCS and hydrogen)
Macro Economic models
Egging 2019 - Paris - NG in the European ET
37

## Slide 38: SET-Nav Patways Sector models + PRIMES Ref: EU Gas demand development (BCM/y)
Chart: 
Reference demand | 443.4155 | 436.4054 | 439.1137 | 426.0651 | 428.3661 | 431.4982 | 437.4476 | 443.9293
Reference production | 130.026 | 118.075 | 103.554 | 88.71 | 71.601 | 67.123 | 65.401 | 60.756
1 bcm = 1 billion m3 = 11.4 TWh = 0.9 Mtoe
Decarbonization – gas demand in:
Transport: up
Industry: down
Building heating: down
Power generation: down
38
Egging 2019 - Paris - NG in the European ET
38

## Slide 39: Gas demand development in the pathways (BCM/y)
Chart: 
Reference demand | 443.4155 | 436.4054 | 439.1137 | 426.0651 | 428.3661 | 431.4982 | 437.4476 | 443.9293
National Champions | 443.9966 | 381.9264 | 331.8732 | 285.1356 | 265.0013 | 251.1459 | 237.4781 | 225.3358
Directed Vision | 442.8355 | 376.0307 | 320.5197 | 270.3674 | 239.9444 | 214.4067 | 192.6318 | 178.805
Localisation | 442.7432 | 386.4181 | 338.195 | 297.065 | 252.013 | 213.7211 | 169.975 | 129.7412
Diversification | 442.7599 | 399.6885 | 363.6821 | 334.5267 | 267.5014 | 207.1778 | 162.3633 | 123.1819
Reference production | 130.026 | 118.075 | 103.554 | 88.71 | 71.601 | 67.123 | 65.401 | 60.756
50% - 75% decrease
1 bcm = 11.4 TWh = 0.9 Mtoe
39
Egging 2019 - Paris - NG in the European ET
39

## Slide 40: EGGM (REKK)
Europe + neighbors
Exogenous demand, supply and capacities
Pipelines, storages, LNG regasification
Monthly resolution
2015-2050
Bio-methane in 2 pathways
Main outputs: gas prices, infrastructure utilization, market agent profits
Global
Calibrated demand, exogenous (initial) capacities
Pipelines, storage, liquefaction, shipping, regasification
Three seasons, 5-year steps
2015-2050
Endogenous demand, supply, capacity investment, utilization, profits
GGM (NTNU/DIW)

## Slide 41: EU28 import dependency (REKK EGMM model)
(Relative) import dependency stabilizes or decreases
In scenarios with significant RES-gas, dependency decreases drastically
41
Egging 2019 - Paris - NG in the European ET
41

## Slide 42: infrastructure Utilization pipelines from Russia (bcm/y) (NTNU DIW GGM model)
Chart: 
| 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | RUS-BLR | RUS-DEU | RUS-TUR | RUS-UKR
Used | 42.8543 | 47.112 | 47.112 | 48.7257 | 41.8684 | 41.8684 | 41.8684 | 41.8684 | 94.9223 | 94.9223 | 94.9223 | 96.8907 | 67.32 | 73.59 | 81.4 | 76.89 | 44.0883 | 41.7027 | 45.6881 | 50.2532 | 49.3513 | 49.4998 | 58.6365 | 58.6365 | 0 | 0 | 32.5522 | 38.6422 | 0 | 0 | 1.4856 | 1.4856
Unused | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19.4227 | 19.4227 | 19.4227 | 17.4543 | 42.68 | 36.41 | 28.6 | 33.11 | 6.9427 | 9.3283 | 5.3429 | 0.77782 | 0.1485 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Yamal Nordstream Turkstream Brotherhood
42
Egging 2019 - Paris - NG in the European ET
42

## Slide 43: infrastructure Utilization pipelines from Africa (bmc/y)
Chart: 
| 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | DZA-ESP | DZA-ITA | LBY-ITA | TUN-ITA
Used | 17.7423 | 18.7745 | 16.2772 | 20.4232 | 13.0973 | 14.6571 | 13.4192 | 14.9047 | 0.30915 | 1.1023 | 0.48873 | 10.1448 | 0 | 0 | 0 | 0 | 9.409 | 13.9039 | 13.9039 | 13.9039 | 7.5796 | 8.8068 | 7.7009 | 5.8263 | 28.9982 | 29.4237 | 30.3293 | 36.9654 | 18.4767 | 12.1242 | 4.7916 | 4.8642
Unused | 7.6774 | 6.6452 | 9.1425 | 4.9965 | 11.6613 | 10.1015 | 11.3395 | 9.854 | 39.0696 | 38.2765 | 38.89 | 29.2339 | 38.0399 | 38.0399 | 38.0399 | 38.0399 | 4.495 | 0 | 0 | 0 | 5.9072 | 4.6799 | 5.7858 | 7.6605 | 7.9672 | 7.5416 | 6.6361 | 0 | 17.8233 | 24.1758 | 31.5084 | 31.4358
Maghreb+Medgaz Galsi Greenstream TransMed
43
Egging 2019 - Paris - NG in the European ET
43

## Slide 44: infrastructure Utilization pipelines from Russia (bcm/y)
Chart: 
| 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | 2020 | 2030 | 2040 | 2050 | Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | RUS-EST | RUS-FIN | RUS-LVA
Used | 0.54714 | 0.46902 | 0.56757 | 0.60189 | 0.31935 | 0.63206 | 0.54556 | 0.39254 | 1.7297 | 1.8462 | 1.9086 | 1.5629 | 3.181 | 5.174 | 5.5727 | 4.5681 | 2.3276 | 2.7415 | 2.7258 | 2.8944 | 1.7429 | 2.3067 | 2.4898 | 2.1163
Unused | 6.2349 | 6.313 | 6.2145 | 6.1802 | 6.3339 | 6.0212 | 6.1077 | 6.2607 | 6.397 | 6.2806 | 6.2181 | 6.5638 | 4.7914 | 2.7983 | 2.3997 | 3.4042 | 5.16 | 4.7461 | 4.7618 | 4.5932 | 5.5801 | 5.0163 | 4.8332 | 5.2066
44
Egging 2019 - Paris - NG in the European ET
44

## Slide 45: infrastructure Utilization regasification (bcm/y) GGM
Chart: 
| Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | Reference | Directed Vision | 2020 | 2030 | 2040 | 2050
Used | 45.1713 | 67.0396 | 53.6725 | 9.1108 | 63.8914 | 0.65787 | 53.4798 | 0
Unused | 178.9913 | 153.6617 | 186.2263 | 227.091 | 176.0074 | 235.5439 | 186.419 | 236.2017
45
Egging 2019 - Paris - NG in the European ET
45
Notes: Peter/Borbala: GGM does not foresee any LNG imports after 2035. What is driving EGMM LNG imports? contracts, other assumptions? Are there some high load months when they occur?
We have global LNG oversupply in the assumptions. Depending on the scenario, if EU production is not substituted with domestic EU RES gas and Russia does not utilize the Ukrainian grid for transit, the missing volumes are substituted from the LNG. We also have some LNG contracts, but this is not the main driving factor.

## Slide 46: Effects on TSOs
Operational income drops by ¾
Upward pressure on tariffs
  May further reduce competitiveness
Decommissioning pipelines
  may distort SOS; possibly not critical when gas share in primary energy so low (?)
46
Egging 2019 - Paris - NG in the European ET
46
Notes: Peter/Borbala: what is IP?
Interconnection Point. Points of infrastructure connecting the TSO-TSO areas. IP related revenue refers to the revenues of TSOs realized on the borders (as opposed to storage, production and distribution points).

## Slide 47: Effects on storages
Without decarbonisation, need for storage grows
  Reference 2020 52 bcm/y  2050 64 bcm/y (+23%)
In scenarios storage usage decreases 50%-75%
  Scenarios: 2050 15-25 bcm/y
  Based on monthly loads, not accounting for intermittency “backup”
47
Egging 2019 - Paris - NG in the European ET
47

## Slide 48: Additional notes
Upward pressure on infrastructure usage tariffs may further reduce gas usage, etc.
Decommissioning & stranded assets?
Gas models have not considered minimum flows and volumes
Gas routing & maintaining pressure in structurally low throughput situations?

## Slide 49: conclusion

## Slide 50: Role for NG in European energy
Do we still need gas after 2040? No (!)
Decarbonization is not our only mission: “100% Renewables” may be the right answer, but it is the wrong question.
Consider NG as part of the future energy mix? Yes
Not considering NG (and CCS) in the transition or as constituents of a low-carbon future energy system may be very expensive.
Keep all options open and aim at a level-playing field with fair incentives pricing in all external effects ranging from climate and health impact to flexibility and security of supply

## Slide 51: Research agenda
future energy system will rely on much broader range of energy supply and transportation technologies
will allow and need more tailored solutions
planning and management much more complex.
Deterministic annual / seasonal average loads will become meaningless metrics.
Gas market / system research will have to explicitly account for much lower time-scales and connect / link to other parts of the energy system
  Sector linkage, carrier substitution, time-scales
  Gas system supporting energy transition
Market design and incentives accommodating new roles

## Slide 52: Some links:
SET-Nav reports, papers, briefs…
  https://www.set-nav.eu
GGM is now open access
  https://www.ntnu.edu/web/iot/ggm
  Model code and data + documentation
NTNU Energy Transition Initiative
  research on transition strategies to a sustainable energy system and low carbon society.
  https://www.ntnu.edu/energytransition
openENTRANCE 2019-2023
  H2020 EU project – SET-Nav II - focus on open model & data
Norwegian Research Council NTRANS 2019-2027
  Energy Transition Strategies – Social acceptance and behavioral aspects

## Slide 53: Thank you
ruud.egging@ntnu.no
Notes: ntnu page
research gate
repec